## Slide 1
stream
SVC on Android, Debugged
A hardware encoder debugging story
Pratim Mallick · Android SDK @ Stream
RTC.ON 2026 · Kraków

## Slide 2
Aug 2026
STREAM
Stream Products
CHAT MESSAGING
VIDEO & AUDIO
ACTIVITY FEEDS
AUTO MODERATION

## Slide 3
Aug 2026
STREAM · RTC.ON 2026
Agenda
01
VP9 SVC 101
What it is, why we need it
02
The Debugging Story
Symptom → Root cause
03
Hardware Capabilities
Can we query the system?
04
Way Forward
Practical solutions

## Slide 4
Aug 2026
01
VP9 SVC 101

## Slide 5
Aug 2026
VP9 SVC 101
What is Scalable Video Coding?
01
Encode
once
1 encoder
1 stream
→
L3T3
S2 · 720p · 30 fps
S1 · 360p · 15 fps
S0 · 180p · 7.5 fps
→
02
SFU drops
layers
No decode
No re-encode
→
720p viewer
180p viewer
SPATIAL
Resolution · 720p → 360p → 180p
TEMPORAL
Frame rate · 30 → 15 → 7.5 fps

## Slide 6
Aug 2026
VP9 SVC 101
Why SVC? (vs Simulcast)
SVC
Phone
1 encode
→
720p
360p
180p
→
SFU
1 stream · 1 encoder · SFU drops layers
SIMULCAST
Phone
3 encodes
→
→
→
720p
360p
180p
→
SFU
3 streams · 3 encoders · more CPU
On mobile, CPU and battery win. SVC is the better fit — if the encoder can actually produce the layers.

## Slide 7
Aug 2026
02
The Debugging Story

## Slide 8
Aug 2026
THE DEBUGGING STORY
The Setup — Everything Works
Android
Publisher
(VP9 HW)
→ L1T3 →
SFU
→
Subscriber
(1)
1 subscriber → SFU requests L1T3 (1 spatial, 3 temporal)
Hardware VP9 encoder handles this fine
Network quality: excellent

## Slide 9
Aug 2026
THE DEBUGGING STORY
3rd Participant Joins — Quality Drops
Android
Publisher
(VP9 HW)
→ L3T3_KEY →
SFU
→
→
Sub 1
Sub 2
Multiple subscribers → SFU switches to L3T3_KEY (3 spatial, 3 temporal)
SFU quality score drops immediately and never recovers

## Slide 10
Aug 2026
THE DEBUGGING STORY
The Symptoms — Hardware VP9 Only
Observed only on hardware VP9. Software VP9 (libvpx) showed none of these.
01
SFU marked the stream as poor
Score fell when the 3rd participant joined — and never recovered
02
Encoder re-created in a loop
Hardware encoder destroyed and recreated ~every 200ms
03
Stats looked starved
targetBitrate reported ~71 kbps at 720×1280

## Slide 11
Aug 2026
DEBUGGING
The Encoder Thrashing Loop
01
QUALITYSCALER
720p → 540p
QP too high
→
02
HW ENCODER
STOP / START ×2
Surface → ByteBuffer
→
03
GCC / BWE
Bitrate drops
Huge frames
→
04
QUALITYSCALER
540p → 720p
QP too low
← back to 720p · repeats every 5–10 seconds
Looked like the bitrate problem. We disabled QualityScaler — the loop stopped. The SFU still marked this stream as poor. So we went deeper.

## Slide 12
Aug 2026
DEBUGGING
Asked for 3 Layers — Encoder Sent 1
ASKED FOR
L3T3_KEY
S2 · 720p
top layer
S1 · 360p
mid layer
S0 · 180p
base layer
→
ENCODER PRODUCED
1 flat stream
720p only
No S1 · No S0 · Nothing to split
~1.4 Mbps sent — not starved
SFU expected three layers. Hardware sent one. Stream marked poor.

## Slide 13
Aug 2026
DEBUGGING
Why Those Symptoms Happened
01
SFU marked the stream as poor
SFU expected 3 spatial layers. Hardware sent 1.
02
Encoder re-created in a loop
QualityScaler flipped 720p ↔ 540p every 5–10s. Each flip recreates the HW encoder twice.
03
Stats looked starved
VP9 SVC stats bug — reports only the base layer, not the total (~1.5 Mbps).
Software VP9 never hit 01 or 02 — it produces real L3T3 layers and never tears down the encoder.

## Slide 14
Aug 2026
03
Querying Hardware
Capabilities

## Slide 15
Aug 2026
HARDWARE CAPABILITIES
MediaCodec SVC Support — Temporal Only
What You Can Query
Supported resolutions & bitrates
Profile levels
Temporal layering schemas (KEY_TEMPORAL_LAYERING)
What You Can't
Spatial layer support
"Does this encoder do L3T3?"
Multi-resolution SVC capability
Android 17 (API 37) adds getSupportedLayeringSchemas() — but only returns temporal schemas like webrtc.svc.l1tN. The platform confirms: hardware SVC = temporal only.

## Slide 16
Aug 2026
04
Way Forward

## Slide 17
Aug 2026
WAY FORWARD
Software VP9 (libvpx) — Pros & Cons
✓ Pros
True L3T3 — all 3 spatial layers
No encoder re-creation issues
SFU quality stays stable
✗ Cons
High CPU → qualityLimitationReason: cpu
Battery drains significantly faster
Frame rate may drop under load
Today's only complete fix for spatial SVC — but the CPU/battery cost is real on mobile.

## Slide 18
Aug 2026
WAY FORWARD
Production Data — Android Is the Outlier
190 Android livestreams from a livestreaming customer — July 2026
Host Type | Median Quality | Poor (<70)
Android app | 89 | 41%
iOS app | 98 | 7%
Web browser | 98 | 6%
OBS / external | 99 | 0.4%
Android VP9 breakdown
HW VP9 (Samsung)
100% poor
Median quality: 30
SW VP9 (libvpx)
28% poor
CPU/battery limited
Neither VP9 path works reliably on Android. Hardware can't do SVC; software drains the device. A 720p cap doesn't help — the encoder is the bottleneck, not resolution.

## Slide 19
Aug 2026
WAY FORWARD
Broadcaster Mode — Server-Side Quality Ladder
Android
Publisher
1 clean HW stream
(H.264 or VP8)
→
Stream Server
(transcodes)
Generates quality
ladder server-side
→
→
→
720p viewer
360p viewer
180p viewer
•
Phone publishes one stream on its best hardware codec — no SVC needed
•
Server generates the adaptive quality ladder viewers need
•
No CPU drain, no missing layers, no encoder re-creation
•
SDK option — opt-in for livestream / broadcast use cases

## Slide 20
Aug 2026
SVC ON ANDROID, DEBUGGED
Takeaways
•
HW VP9 → temporal SVC only, spatial layers silently missing
•
SW VP9 → real SVC, but CPU/battery cost too high on mobile
•
Neither path works — 100% HW failure, 28% SW failure in prod
•
Broadcaster mode = phone sends 1 stream, server makes the ladder
•
No API to query spatial SVC — you find out from the bitstream

## Slide 21
Thank you
Questions?
Pratim Mallick · Stream
Aug 2026